## Slide 1: ECE 593 Fundamentals of Pre-Silicon Validation
Venkatesh Patil Electrical and Computer Engineering Department Maseeh College of Engineering and Computer Science

## Slide 2: Design and Verification of Asynchronous FIFO Winter 2025 – Session 2 – Group 10
Aadityasingh Chouhan Moulya Raju Machohalli Thimmaraju
Email Id : aadityac@pdx.edu Email Id : moulya@pdx.edu
PSU ID : 960054443 PSU ID : 947898393
Rakshith Rajashekhara Bharadwaj Subramanya Dhanajaya
Email Id : rbharadw@pdx.edu Email Id : subrama@pdx.edu
PSU ID : 929940720 PSU ID : 941540243

## Slide 3: Project Introduction
Rakshith Rajashekara Bharadhwaj
System Verilog
  FIFO Read
  Testbench
Class Based Verification
  Finalized RTL
  Class based Testbench
UVM Verification Environment
  UVM Architecture
  Top Module
  Test
Aadithyasingh Chouhan
System Verilog
  FIFO Memory
  Synchronizer
Class Based Verification
  Generator
  Interface
  Environment
UVM Verification Environment
  Environment
  Interface
  Sequence

## Slide 4: Project Introduction
Subramanya Dhanajay
System Verilog
  FIFO Write
Class Based Verification
  Driver
  Transaction
  Scoreboard
UVM Verification Environment
  Agent
  Scoreboard
  Transaction
  HLDS Document
Moulya Raju
System Verilog
  Top Design
Class Based Verification
  Randomized Test cases
  Coverage
  Verification Document
UVM Verification Environment
  Coverage
  Test cases
  Bug Injection
  Verification Document

## Slide 5: Project Introduction
The Asynchronous FIFO (First-In-First-Out) is a type of memory buffer used in digital systems to transfer data between two clock domains operating at different frequencies. It ensures smooth data transfer while handling clock domain crossing issues.
The design typically consists of write and read pointers, memory storage, control logic for full and empty flags, and synchronization mechanisms to prevent metastability when transferring control signals between clock domains
Asynchronous FIFOs are widely used in high-speed communication interfaces, data buffering between different clock domains in FPGA and ASIC designs, and in systems requiring reliable data transfer with varying clock rates.
The primary challenges include metastability, pointer synchronization, and ensuring data integrity. These are addressed using Gray-coded pointers, dual-port memory, and proper synchronizer circuits.

## Slide 6: Specifications
Producer Clk frequency (clk 1): 60 MHz
Consumer Clk frequency (clk 2): 100 MHz
Maximum write burst size: 1024.
Duty cycle: 50%
No. of Idle cycle between successive writes = 3
No. of Idle cycle between successive reads = 2

## Slide 7: Specifications
Time required to write one data item: 4 x (1/60MHz) = 66nsec
Time required to write all the data in the burst = 1024 x 66nsec= 67584nsec
Time required to read one data item = 3 x (1/100MHz) = 30nsec
So, for every 30 n, the consumer block is going to read one data in the burst. So, in a period of
67584nsec, a maximum 1024 number of data items can be written.
Therefore, the number of data items can be read in a period of 67584nsec = 67584nsec/30nsec=2252.
The remaining number of bytes to be stored in FIFO = 2252-1024 = 1228 so a depth of 11 is required.

## Slide 8: Design Implementation
Talk about design Implementation
  Source of design
  Your groups contribution over the source of design
  Quick specification of your design to be verified

## Slide 9: Design Implementation
Empty Condition:
The FIFO is empty when there is no valid data to read.
This happens when the read pointer catches up to the write pointer.
The empty flag is asserted, preventing further reads until new data is written.
Proper synchronization ensures the read domain correctly detects the empty condition.
Full Condition:
The FIFO is full when all available memory locations are occupied.
This occurs when the write pointer reaches the read pointer after completing a full cycle (considering circular buffer implementation).
The full flag is asserted, stopping further writes until space is available.
Gray-coded pointers and synchronization help avoid incorrect full flag assertions.

## Slide 10: Design Implementation
An additional bit is utilized to determine the FULL and EMPTY conditions.
Gray coding is used, and the most significant bit (MSB) of the pointers is compared to assess these states.
During reset, both the read and write pointers are initialized to zero.
After data is written to the memory at the address indicated by the write pointer, the pointer advances to the next location.
The FIFO is considered empty when the read and write pointers hold the same value, either at reset or when the read pointer catches up to the write pointer.
The FIFO becomes full when the write pointer wraps around and matches the read pointer again.

## Slide 11: Design Implementation

## Slide 12: Class based Verification
Transaction Class

## Slide 13: Class based Verification
Driver
Generator

## Slide 14: Class based Verification
Scoreboard
Monitor

## Slide 15: UVM based Verification

## Slide 16: UVM based Verification
Sequencer
Sequence item

## Slide 17: UVM based Verification
Monitor
Driver

## Slide 18: UVM based Verification
Scoreboard
Agent

## Slide 19: UVM based Verification
Test
Environment

## Slide 20: UVM based Verification
Top
Coverage

## Slide 21: Coverage

## Slide 22: SV Simulation Results
SV Class based Results

## Slide 23: UVM Simulation Results

## Slide 24: Challenges faced
During our initial test run, we quickly identified an issue. The `data_out` value was incorrectly received as 'x' due to a faulty connection during setup, leading to unexpected behavior. It was frustrating to see the read address increment values completely misaligned.
After completing the read and write transfers, we anticipated the correct assertion of full and empty signals, but they failed to appear. Each read transfer was supposed to extract the latest data from the monitor and driver, yet the system remained unresponsive, seemingly stuck without updating properly.
A significant problem was the lack of an error detection and correction mechanism, making it impossible to verify the asynchronous FIFO accurately. Additionally, race conditions between the write and read pointers caused instability and confusion. The most frustrating part was the system's failure to revert to a previously functional state, leaving us with a broken setup and no immediate resolution.

## Slide 25: Conclusion
The design and verification of an asynchronous FIFO using SystemVerilog (SV) and Universal Verification Methodology (UVM) ensure accuracy and reliability.
Key techniques include functional coverage analysis, assertions, and a well-structured design approach.
SV and UVM enhance verification by providing modularity, reusability, and scalability.
Directed testing focuses on critical scenarios, while random testing helps identify edge cases.
By integrating these methodologies, the design meets its requirements and functions reliably.
This project achieved approximately 95% coverage, including both code and functional coverage.

## Slide 26: References and Citations
1. S. Cummings, "FIFOs: Fast, predictable, and deep," in Proceedings of SNUG, 2002. [Online]. Available:http://www.sunburst-design.com/papers/CummingsSNUG2002SJ_FIFO1.pdf
2. S. Cummings, "FIFOs: Fast, predictable, and deep (Part II)," in Proceedings of SNUG, 2002. [Online]. Available: http://www.sunburst-design.com/papers/CummingsSNUG2002SJ_FIFO2.pdf
3. Putta Satish, "FIFO Depth Calculation Made Easy," [Online]. Available: https://hardwaregeeksblog.files.wordpress.com/2016/12/fifodepthcalculationmadeeasy2.pdf
4. A. Author et al., "Title of the Paper," in Proceedings of the Conference, 2015, pp. 123-456. [Online]. Available: https://ieeexplore.ieee.org/abstract/document/7237325.

## Slide 27: References and Citations
5. M. Last Name et al., "Designing Asynchronous FIFO," [Online]. Available: https://d1wqtxts1xzle7.cloudfront.net/56108360/EC109-libre.pdf.
6. A. Author et al., "Title of the Paper," in Proceedings of the Conference, 2011, pp. 789-012. [Online]. Available: https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=6041338
7. Aldec website https://www.aldec.com/en/company/blog/168--verification-effectiveness-with-riviera-pro-systemverilog-randomized-layered-testbench
8. [1] Chip Verify. [Online]. Available: https://www.chipverify.com